## Slide 1
Harmonization is Key
Omar Frits Eriksson
Deputy Secretary General &
Dean of the World-Wide Academy

## Slide 2: Harmonization is Key
Shipping is by its very nature mobile and global.
Shipowners may be willing to equip their new-buildings with state-of-the-art technology to maximize their competitive advantage and operational safety, but they are reluctant to spend money on multiple sets of equipment just because different regions of the world have developed their own digital solutions which are incompatible with each other.
Such incompatibility is a barrier to safe and sustainable global movement of vessels and will ultimately reduce the efficiency of the transport chain.
This is why we must harmonize the standards for digital solutions world-wide.
Indiustry is screaming for standards – IALA, IHO and IMO have the solution

## Slide 3: IALA Maritime Buoyage System (MBS)

## Slide 4: Lateral Marks
Denote the port and starboard sides of a channel
Check buoyage direction
Optional topmarks
Preferred channel marks with Composite Group Flashing lights (2+1) can be used where a channel divides
Can be synchronised
Region A Region B
Same can-shaped optional topmark
Buoyage direction
Region A lateral marks

## Slide 5: Cardinal Marks – Both Regions
Named after the quadrant in which it is laid
Pass the mark on the named side
Must carry lights (Q/VQ; Q3; Q6; Q9) and topmarks
Used:
  Indicate deepest water
  Indicate safe side to pass
  Draw attention to feature (e.g. channel bend or end of a shoal)
  Note: too many Cardinal Marks in close proximity can confuse the mariner (IALA MBS 3.2.4)

## Slide 6: Isolated Danger Mark
Built on or moored close to an isolated danger
Must have navigable water all round it
Pillar or spar buoy
Must carry topmark (2 black spheres one above the other)
Gp Fl 2 (Fl (2)) light (if lit)

## Slide 7: Safe Water Mark
Indicates navigable water all round
Used:
  Fairway/landfall buoy
  Centre line in TSS
  Mid-channel marks
Top mark red sphere (optional)
Light
  Isophase
  Occulting
  Long flash every 10 seconds
  Morse “A”

## Slide 8: Flash Characters
Long flash – more than 2 seconds duration
Single flash of about 1 second
Quick flash – period about once a second
Very quick flash – period about half a second
Isophase – equal light and dark
Occulting – more light than dark
Morse code character
Alternating colours
Fixed – not used

## Slide 9: How was harmonization of the buoyage system achieved?

## Slide 10: Four steps of harmonization
Define and publish the basic principles (technology agnostic and durable)
Provide guidance on how contemporary technologies can be utilized to apply the principles
Create a desire or an obligation to follow the principles
Publish how the principles have been implemented in any given geographical area
Notes: In case of Aids to Navigation the benefits of harmonization were obvious to mariners who travel world-wide, and are constantly trying to find their way using all available information. Such a concept minimizes confusion and maximises the situational awareness of the navigator
In the case of e-Navigatio, the benefits are a bit more abstract, and seem to be difficult for navigatiorsto understand.

## Slide 11: Four steps of harmonization
Define and publish the basic principles (technology agnostic and durable)
Notes: In case of Aids to Navigation the benefits of harmonization were obvious to mariners who travel world-wide, and are constantly trying to find their way using all available information. Such a concept minimizes confusion and maximises the situational awareness of the navigator
In the case of e-Navigatio, the benefits are a bit more abstract, and seem to be difficult for navigatiorsto understand.

## Slide 12: Four steps of harmonization
2. Provide guidance on how contemporary technologies can be utilized to apply the principles
IALA Guidelines (how to do it)
Ex: Incadescent lamps versus LED´s

## Slide 13: Four steps of harmonization
3. Create a desire or an obligation to follow the principles
IALA Standards and Recommendations (what to do)
IMO - SOLAS Regulation 13 footnote

## Slide 14: Four steps of harmonization
4. Publish how the principles have been implemented in any given geographical area
The Sea Chart (IHO)
Enables discovery/usage by seafarers

## Slide 15: Global Harmonization (A & B)

## Slide 16: MBS analogy in e-Navigation – digital services?
Define and publish the basic principles (technology agnostic and durable)
Notes: In case of Aids to Navigation the benefits of harmonization were obvious to mariners who travel world-wide, and are constantly trying to find their way using all available information. Such a concept minimizes confusion and maximises the situational awareness of the navigator
In the case of e-Navigatio, the benefits are a bit more abstract, and seem to be difficult for navigatiorsto understand.

## Slide 17: IHO S-100 Geospatial Information Registry
http://s100.iho.int/S100/productspecs

## Slide 18: Five types of e-Navigation “specifications”
S-100, S-200 …
Data Product
Specifications
Maritime Service
Descriptions
Technical Service
Specification
Technical Service Design
Description
Technical Service Instance
Description
IMO
IHO (S-100)
IALA (S-200)
IALA
IALA
IALA

## Slide 19: Five types of e-Nav “specifications/descriptions”
S-100, S-200 …
Data Product
Specifications
Maritime Service
Descriptions
Basic Principles
Technology Agnostic
Technical Service Design
Description
Technical Service Instance
Description
IMO
IHO (S-100)
IALA (S-200)
IALA
IALA
IALA
Technical Service
Specification
Technology Selection
How to do…
(IALA Guidelines)
(Blueprint)
Actual Implementation
(Sea Chart)
What to do
(IALA
Recommendations)

## Slide 20: I am Tony I want to start my own business using e-Navigation principles

## Slide 21: What type of business to select? - Tug service? - VTS service? - AtoN service? - Pizza service?

## Slide 22: What type of producta should I offer? - Pizza Bolognese? - Pizza Diavolo? - Pepperoni Pizza (my mama´s recipe)

## Slide 23: What is my Pizza service Concept? (technology agnostic) - Orders by telecommunication - Delivered to shipside - Within 17 minutes - Firmly packaged & still warm

## Slide 24: What technology and design? (Blueprint) - Stone furnace - Cardboard packaged - Delivered by Scooter - Pay by credit card - Domino´s look alike

## Slide 25: I must advertise (Yellow Pages) - Establish Identity - Enable discovery - Publish endpoints - Conduct business

## Slide 26: Now I have several instances

## Slide 27: Four steps of harmonization
Define and publish the basic principles (technology agnostic and durable)
Provide guidance on how contemporary technologies can be utilized to apply the principles
Create a desire or an obligation to follow the principles
Publish how the principles have been implemented in any given geographical area

## Slide 28: Global harmonized Connectivity requires more
5. Secure a share of our natural resources (frequency bandwith for digital channels)
Connectivity is the key enabler
Without harmonized world-wide interoperable connectivity solutions there is no e-Navigation
Notes: In case of Aids to Navigation the benefits of harmonization were obvious to mariners who travel world-wide, and are constantly trying to find their way using all available information. Such a concept minimizes confusion and maximises the situational awareness of the navigator
In the case of e-Navigatio, the benefits are a bit more abstract, and seem to be difficult for navigatiorsto understand.

## Slide 29: Projects - SESAME II You want to start your own business 23 mio. NO$ Open up – otherwise it is not e-Navigation

## Slide 30
Connect:
E-mail: omar.eriksson@iala-aism.org
LinkedIn: Omar Frits Eriksson
Twitter: OMaritime
Mobile: +33 6 31 17 76 42