## Slide 1: Aids to Navigations Availability Rate (AAR) calculations in the Finnish waters

## Slide 2: Waterway classification system in Finland
Channel class | Service level | Marking
VL1 | It can be used in all visibility conditions. Winter navigation with ice-strengthened vessels or supported by icebreaking assistance is possible. | All types of aids to navigation are used on the channel. Fixed AtoNs constructed in the water are also built as needed. The channel is illuminated. The channel markings enable navigation in all conditions.
VL2 | The usability of the channel at night or in poor visibility conditions may be partially restricted. The channel is not designed with winter navigation in mind. | All types of aids to navigation is used on the fairway, but normally no fixed AtoNs is constructed in the water . The fairway is illuminated or aids to navigation is equipped with at least light reflectors. Fixed radar targets are limited.
VL3 | The usability of the channel in poor visibility conditions may be partially restricted. The channel is not designed with winter navigation in mind. | The marking is primarily based on the use of leading lines and floating Atons. The fairway is illuminated or equipped with a sufficient number of reflectors for nighttime navigation.

## Slide 3: Waterway classification system in Finland
VL4 | The usability of the fairway in all visibility conditions is at least satisfactory. The fairway is designed to be used only during open water conditions | The marking is based on the use of leading lines, floating AtoNs (buoys), and daymarks. Generally, it is not illuminated. The fairway has a sufficient number of reflectors for nighttime navigation.
VL5 | The usability of the fairway in all visibility conditions is at least satisfactory. The fairway is designed to be used only during open water conditions | The marking is based on the use of floating AtoNs (buoys) and daymarks. It is not illuminated.
VL6 | The usability of the fairway in all visibility conditions is at least satisfactory. The fairway is designed to be used only during open water conditions | The marking is based on the use of floating AtoNs (buoys) and daymarks on a case-by-case basis. It is not illuminated.

## Slide 4: Waterway classification system in Finland

## Slide 5: Availability Rate Categories
Category 1 = Includes channel class VL 1 illuminated aids to navigation, minimum functionality 99.8%.
  Sailing season all year round
Category 2 = Includes channel class VL 1 unlit aids to navigation and VL2-VL6 illuminated aids to navigation, minimum functionality 99.0%.
Sailing season:
  VL 1: All year round
  VL 2-6 (Sea area: Vironlahti-Merikarvia, inland waters south of Oulujoki water system): 1.5-30.11
  VL 2-6 (Sea area: Merikarvia-Tornio, inland waters: Oulujoki water system and lake areas north of it): 1.6-15.11
  Saimaa Canal and deep-water channel: Saimaa Canal traffic season: 1.6-30.12

## Slide 6: Availability Rate Categories
Category 3 = VL 2-VL 3 unlit aids to navigation, minimum functionality 97.0%
Sailing season:
  VL 2-6 (Sea area, Vironlahti-Merikarvia. Inland waters south of the Oulujoki river basin.) 1.5-30.11
  VL 2-6 (Sea area: Merikarvia-Tornio. Inland waters: Oulujoki river basin and lakes north of it.) 1.6-15.11
  Saimaa Canal and deep channel on the Saimaa Canal navigation season 1.6-30.12
The minimum operational requirement for each fixed AtoN is a 95% uptime per sailing season and for visual obstruction (vegetation) faults on fixed Atons in VL3-6, 90%.
Aton faults outside the sailing seasons is not included in the calculations and Atons under construction.

## Slide 7: Sailing seasons in Finland waters
VL 1= All year around