## Slide 1: Candidate technology for speech and data
dPMR trial 10th of December 2019 Rotterdam
IALA
ENAV26

## Slide 2: dPMR trial
Why?
Demands and wishes
Technology
Goal
Results

## Slide 3: Why
Limited space in Appendix 18
(digital) developments
Incidents
Efficient use of frequency
Higher level of safety

## Slide 4: Demands and wishes
Users
  Easy to use
  Limit mistakes
Long migration period
Independence
  Manufacturer
  Supporting technology
    GPS (timing)
    Codec
Keep current functionality
Costs
Impact
Available technology
Future-proof
(Cyber) security
Support of Smart Shipping
Harmonized
Open standards

## Slide 5: Transfer data/information
Notes: Pictures show that we have a goal or intention to transfer a message. This could be done through different channels like voice and digital with less or more data in it. At the end it is combined again to the message and hopefully will end in the right reaction.
The other are the old communication (almost none) the explosion of communication and hopefully at the end get it structured

## Slide 6: Candidate technologies
5G
LTE-M
Satellite
Tetra
NXDN
DMR
dPMR
….

## Slide 7: Chosen technology for trial
dPMR
  Seems to fulfil all demands
  Must be adjusted/expanded for maritime use

## Slide 8: Purpose of first trial
First acquaintance
User experience
Technology
Demands and Wishes
Future

## Slide 9: Cooperation
Port of Rotterdam
  Operator / mariner
  Ship / VTS centre
Rijkswaterstaat
  Coordination
  Finance
Agentschap Telecom (ITU)
  Analyse spectrum
dPMR Association
  Technical support (CML)

## Slide 10: Area

## Slide 11: Equipment
Three mobile radios
Three porto’s
Two different brands
  iCOM
  Kenwood
Used by landmobile
  ETSI standard

## Slide 12: Results
Positive remarks from:
  operator / mariner
  Agentschap Telecom (ITU)
  Visitors
Additional demands and wishes
Calculated coverage VTS centre <-> Ship 23 km
Tested with ideal circumstances
Analog Sound
Digital Sound

## Slide 13: Remarks operator - mariner
Easier to listen to / less tiring
Better voice quality
Noise reduction
Detection of abnormalities

## Slide 14: Remarks
Shut down a transmitter remotely
MMSI & CallSign integration
Changes if there are more ships
Switch Digital <-> Analog
Limit time for conversation
GMDSS integration
Detect interference
Detection poor signal
Multicast / diversity
(Half)duplex connections
Dual watch functionality
Dedicated ¼ channel for AIS-GPS signal
Tested English and Dutch
Could functionalities been combined (DSC, ATIS, AIS, VDES, VHF radio digital/analog, …)
Tested with ideal circumstances
Notes: At the moment this is a manufacturer feature, it is described in the dPMR Association documents and implemented by Icom, but not known that others have done this.
Transmit own ID’s are included in each transmission, and repeated during the transmission to allow for “late entry.
If there are more ships the same happens as with analog. The same FM capture effect will occur.
Both tested equipment support mixed mode, however there is a debate as to how useful this feature actually is. If the channel bandwidth for analogue and digital is the same, or the digital channel is on the same frequency centre as the analogue one, then this has some merit, but when they are different (as in this case) it gets more complicated as one analogue channel now covers 4 or 5 digital ones.
All PMR/LMR radios support a transmit timeout feature, usually programmable. Some have also an additional Tx timeout inhibit, so that if the timeout is triggered, it cannot re-transmit for a specific period (usually these values are set to 60 seconds and 10 seconds) but are configurable. The dPMR standard specifies a maximum Tx timeout time of 3 minutes
These are implemented in Icom products, maybe available as an accessory on Kenwood.
This is similar to analogue, if the RF signal is “signal quality indicator” if the manufacturer choses.
RSSI can function in exactly the same way as analogue, but can be enhanced as the radio can tell how many bit errors it is having to correct, so this can alo be presented to the user as a “signal quality indicator” if the manufacture choses.
Same as for analogue.
This means half duplex, ie repeater operation, then all LMR/PMR radios support this mode as standard.
All radios have a feature called “channel scan” which is an enhanced version of “dual watch” – some also have a “priority channel scan”, which is more like “dual watch”. Essentially this is a feature that can be implemented by the manufacturer if they want to, it’s not part of the dPMR standard
Various data facilities are available in the standard, and implemented by some manufactures.
dPMR radios are currently in use throughout the world with multiple languages. The vocoder used is language agnostic.
Certainly feasible from an engineering point of view (VDES box already integrates AIS, ASM, VDE, DSC). Some complications when it comes to certification, otherwise it’s a commercial decision by manufactures and customers.
The dPMR technology has been commercially deployed in the PMR/LMR environment for many years with no issues

## Slide 15: Developments
Presentation(s)
  IALA
  CEPT – FM58
Work item at CEPT – FM58
  Report - Analyses of different digital radio protocols for use in maritime communication - from Estonia (Cybernetica)
  Report - Test measurements on maritime VHF voice radio communication – from Estonia
ETSI will produce a Technical Report
Attention within The Netherlands
Regulatory issues

## Slide 16: Future
Report(s)
  Agentschap Telecom (ITU)
  CML
  CEPT – FM58
Gain more experience
  Users
  Technology
  Different conditions
Involve more parties
  Manufacturers
  Suppliers
  Government/authorities
Monitor developments
Roadmap / Project plan
Identification/authorization transmitter

## Slide 17: Happy users…
Any Questions

## Slide 18: Questions
Port of Rotterdam
Martijn Ebben
M.Ebben@portofrotterdam.com
CML
Derek Love
dlove@cmlmicro.com
Rijkswaterstaat
Jeffrey van Gils
Jeffrey.van.gils@rws.nl
This trial was made possible by: