## Slide 1: CARPET-VTS development
13-09-2013
1
Arne Theil
arne.theil@tno.nl
+31-88-8664070

## Slide 2: CARPET-VTS development
13-09-2013
2
History
Wish list response
TNO proposal
Conclusions

## Slide 3: 1. History
13-09-2013
3
28 september 2010: IALA → TNO: ‘Can TNO upgrade CARPET v2?’
1 februari 2011: TNO → IALA: ‘Can IALA support the business case?’
30 januari 2012: TNO presentation during IALA subcommittee. Prior to this meeting, TNO has sent-out wish lists.
Key questions:
What extensions must the new version of CARPET have?
How is the development of the new version going to be financed?

## Slide 4: 2. Wish list
13-09-2013
4
There is agreement as well as disagreement.

## Slide 5: 2. Wish list response
13-09-2013
5
 | A | B | C | D | E | F | G
Modelling of latest generation solid state coherent VTS radar |  |  |  |  |  |  | 
PRF/RF/pulslength/pulse compression agility |  |  |  |  |  |  | 
Import Doppler filter coefficients, non standard Doppler filtering |  |  |  |  |  |  | 
Modelling of Terma’s frequency diversity |  |  |  |  |  |  | 
FMCW |  |  |  |  |  |  | 
Siting tool, modelling of a radar network |  |  |  |  |  |  | 
STC and other receiver characteristics (e.g. lin/log, limited number of bits) |  |  |  |  |  |  | 
‘Production tool’, command interface |  |  |  |  |  |  | 
Pass/fail verdict that relates to IALA requirements |  |  |  |  |  |  | 
Time side-lobes |  |  |  |  |  |  | 
Shipborne radar |  |  |  |  |  |  | 

## Slide 6: 2. Wish list response
13-09-2013
<number>
 | A | B | C | D | E | F | G
Advanced sea clutter model |  |  |  |  |  |  | 
Linux version |  |  |  |  |  |  | 
More extensive specification of loss factors |  |  |  |  |  |  | 
Google earth |  |  |  |  |  |  | 
Radial velocity averaging |  |  |  |  |  |  | 
Extended target |  |  |  |  |  |  | 

## Slide 7: 3. TNO proposal
Modeling of the latest generation solid state coherent VTS radars Consequences: complex waveform (RF/PRF/pulse length agility), post-detection binary integration, extensive loss factor specification, (partially) encrypted settings files, feedback of OEMs is necessary
Non point-like target model
More advanced modern GUI and graphics
13-09-2013
<number>

## Slide 8: 4. Conclusions
The new CARPET-VTS will be able to assess the performance of the latest generation coherent VTS radar systems
After the modernisation of CARPET, future steps, such as the analysis of radar networks can be taken more easily
13-09-2013
7